## Slide 1: Basic network simulations using ns - 2
Presented by- Shanawaz Ali
Samarth Pratap Singh
Pradipta Kumar Sahoo
Vinay Kumar
Submitted to- Prof. Neeraj Tyagi
Dr. Mayukh Sarkar
Dr. Rajitha B

## Slide 2
Network simulation (NS) is one of the types of simulation, which is used to simulate the networks.
It provides simulation for routing and multicast protocols for both wired and wireless networks.
In ns2, C++ is used for detailed protocol implementation and Otcl is used for the setup.
Introduction

## Slide 3
Goal Of This Project
Understand how to write Tcl scripts to simulate simple network topologies and traffic patterns in NS-2.
Analyze the trace files and understand how to evaluate the performance of networking protocols and operations using :
XGraph tool for forming variable graphs and Netnam tool used for visualization .

## Slide 4
Protocols used in the project
TCP(Transmission Control Protocol)-
A communications standard that enables application programs and computing devices to exchange messages over a network.
Connection Oriented
Slower than UDP
Reliable connection
E.g.: Sending mails, downloading files

## Slide 5
UDP (User Datagram Protocol)
Used to establish low-latency and loss-tolerating connections between applications on the internet.
Unreliable
Not connection oriented
UDP speeds up transmissions by enabling the transfer of data before an agreement is provided by the receiving party.
E.g. - video calls, video games

## Slide 6
Protocols used for creating traffic in a network
FTP(File Transfer Protocol)
It is a application layer protocol
Refers to a group of rules that govern how computers transfer files from one system to another over the internet.
E.g. Businesses use FTP to send files between computers, while websites use FTP for the uploading and downloading of files from their website's servers.

## Slide 7
CBR(Constant Bit Rate)
it is used along with TCP and UDP to design the traffic source behavior of packets.
CBR provides low latency traffic with predictable delivery characteristics for telephony and also native voice applications.
It also offer support for timing sensitive traffic.
It utilizes the full capacity of channel also to provide high quality service.

## Slide 8
n0
n1
#Create a simulator object # (Create event scheduler) set ns [new Simulator]
Step 1:
Step 2:
#Open trace files set f [open out.tr w]
$ns trace-all $f
Name of scheduler
Simple two node wired network

## Slide 9
#Create two nodes set n0 [$ns node] set n1 [$ns node]
Step 3:
Step 4:
#Create a duplex link between the nodes
$ns duplex-link $n0 $n1 1Mb 10ms DropTail
n0
n1
Simple two node wired network

## Slide 10
11
#Create a simulator object
set ns [new Simulator]
#Open trace files
set f [open out.tr w] $ns trace-all $f
#Define a 'finish' procedure
proc finish {} {
global ns f $ns flush-trace close $f exit 0
}
#Create two nodes
set n0 [$ns node] set n1 [$ns node]
#Create a duplex link between the nodes $ns duplex-link $n0 $n1 1Mb 10ms DropTail
#Call the finish procedure after 5 seconds of simulation time
$ns at 5.0 "finish“
#Run the simulation $ns run
But we have no traffic!
Simple two node wired network

## Slide 11
n0 n1
udp
#Create a UDP agent and attach it to node n0 set udp0 [new Agent/UDP]
$ns attach-agent $n0 $udp0
Adding traffic to the link

## Slide 12
n0
n1
udp
# Create a CBR traffic source and attach it to udp0
set cbr0 [new Application/Traffic/CBR]
$cbr0 set packetSize_ 500
$cbr0 set interval_ 0.005
$cbr0 attach-agent $udp0
cbr
CBR: constant bit rate
Adding traffic to the link

## Slide 13
n0
n1
udp
cbr
#Create a Null agent (a traffic sink) and attach it to node n1
set null0 [new Agent/Null]
$ns attach-agent $n1 $null0
null
Adding traffic to the link

## Slide 14
n0
n1
udp
cbr
#Connect the traffic source with the traffic sink
$ns connect $udp0 $null0 #Schedule events for the CBR agent
$ns at 0.5 "$cbr0 start"
$ns at 4.5 "$cbr0 stop”
$ns at 5.0 "finish"
$ns run
null
Adding traffic to the link

## Slide 15
Packet tracing:
On all links:
$ns trace-all [open out.tr w]
On one specific link: $ns trace-queue $n0 $n1$tr
<Event> <time> <from> <to> <pkt> <size> -- <fid> <src> <dst> <seq> <attr>
+ | 1 0 2 cbr | 210 ------- 0 0.0 | 3.1 0 | 0
- | 1 0 2 cbr | 210 ------- 0 0.0 | 3.1 0 | 0
r | 1.00234 0 | 2 cbr 210 ------- | 0 0.0 | 3.1 0 0
Event “+”: enqueue, “-”: dequeue; “r”: received
Record Simulation Trace

## Slide 16
Event | Time | From Node | To Node | Pkt type | Pkt size | Flags | Fid | Src Address | Dest Address | Seq. Num | Pkt ID
Address in “node.port” format
Sequence no. can repeat Pkt ID is always unique
User can set Flow ID in Otcl script for each source
cbr-tcp
+ =enqueue
- =dequeue
r = recv (at the output of the link)
d = dropped
Trace File Format

## Slide 17
1
2
4
5
6
7
8
3
Sink1
Sink2
Sink3
TCP
FTP
TCP
FTP
TCP
FTP
8mbps
8mbps
16mbps
Case - I

## Slide 18
NAM Output

## Slide 19
Packet Delivery Ratio

## Slide 20
Packet Loss Ratio

## Slide 21
End-To-End Delay

## Slide 22
1
2
4
5
6
7
8
3
Sink1
Sink2
null
TCP
FTP
TCP
FTP
UDP
CBR
8mbps
16mbps
8mbps
2Mbps
20Mbps
4Mbps
5Mbps
5Mbps
10Mbps
4Mbps
Case - II

## Slide 23
NAM Output

## Slide 24
Packet Delivery Ratio

## Slide 25
Packet Loss Ratio

## Slide 26
End-To-End Delay

## Slide 27
1
2
4
5
6
7
8
3
Sink1
null1
null2
TCP
FTP
UDP
CBR
UDP
CBR
8mbps
8mbps
9mbps
20Mbps
23Mbps
23Mbps
8Mbps
10Mbps
15Mbps
15Mbps
Case - III

## Slide 28
NAM Output

## Slide 29
Packet Delivery Ratio

## Slide 30
Packet Loss Ratio

## Slide 31
End-To-End Delay

## Slide 32
Future Work
Will going to explore on wireless networks.
Protocols related to wireless networks are- DSR, AODV, AOMDV, DSDV, OLSR
Also going to study about various other simulator like- GNS3 , Qualnet, Opnet etc.

## Slide 33: Thank you